## Slide 1: EE 303 Energy Systems and Power Electronics Power Flow
GRA: Prashant Tiwari
Advisor: Dr. Zhaoyu Wang
1113 Coover Hall, Ames, IA
wzy@iastate.edu
ECpE Department

## Slide 2: Power Flow Analysis
ECpE Department
The power flow problem is a very well-known problem in the field of power systems engineering, where voltage magnitudes and angles for one set of buses are desired, given that voltage magnitudes and power levels for another set of buses are known.
A power flow solution procedure is a numerical method that is employed to solve the power flow problem.
The power flow solution contains the voltages and angles at all buses, and from this information, we may compute the real and reactive generation and load levels at all buses and the real and reactive flows across all circuits.
The above terminology is often used with the word “load” substituted for “power,” i.e., load flow problem, load flow solution procedure, load flow program, and load flow solution.

## Slide 3: Terminologies
ECpE Department
Bulk high voltage transmission systems are always comprised of three phase circuits.
However, under balanced conditions (the currents in all three phases are equal in magnitude and phase separated by ), we may analyze the three-phase system using a per-phase equivalent circuit consisting of the ‘A-phase’ and the ‘neutral conductor’.
Per-unitization of a per-phase equivalent of a three phase, balanced system results in the per-unit circuit.
It is the per-unitized, per-phase equivalent circuit of the power system that we use to formulate and solve the power flow problem.

## Slide 4: Terminologies
ECpE Department
Bulk high voltage transmission systems are always comprised of three phase circuits.
However, under balanced conditions (the currents in all three phases are equal in magnitude and phase separated by ), we may analyze the three-phase system using a per-phase equivalent circuit consisting of the ‘A-phase’ and the ‘neutral conductor’.
Per-unitization of a per-phase equivalent of a three phase, balanced system results in the per-unit circuit.
It is the per-unitized, per-phase equivalent circuit of the power system that we use to formulate and solve the power flow problem.
It is convenient to represent power system networks using the so-called one-line diagram (per-phase equivalent), but without the neutral conductor.

## Slide 5: Terminologies
ECpE Department
The figure represents the one-line diagram of 3- Bus System.
Minimum set to define a network is voltages.
Given a set of power injections & voltages, for all buses find voltage angle and magnitudes.

## Slide 6: Terminologies
ECpE Department
For each bus i, there are four possible variables
Based on what is known/unknown, we can classify buses into three categories.
  PV Bus – Generator Bus
  PQ Bus – Load Bus
  Slack (Swing) Bus – Reference Bus
Slack / Swing Bus is a mathematical artifact. Note: Slack bus is also a Generator Bus.
An injection is the power, either real or reactive, that is being injected into or withdrawn from a bus by an element.
We define a positive injection as one where power is flowing from the element into the bus (i.e., into the network); a negative injection is then when power is flowing from the bus (i.e., from the network) into the element.

## Slide 7: Terminologies
ECpE Department
We define a positive injection as one where power is flowing from the element into the bus (i.e., into the network); a negative injection is then when power is flowing from the bus (i.e., from the network) into the element.

## Slide 8: Terminologies
ECpE Department
 | Known Value | Unknown Value
PQ (Load Bus) |  | 
PV (Gen Bus) |  | ,
Slack (Swing Bus) | , | ,
 | Known Value | Unknown Value
PQ (Load Bus) |  | 
PV (Gen Bus) |  | 
Slack (Swing Bus) |  | 
Note:
N: number of buses in a network
number of Generator Buses
Swing Bus: 1
PV Bus:
PQ Bus: N-

## Slide 9: Network Matrix – Admittance Matrix
ECpE Department
Where,

## Slide 10: Contd…
ECpE Department
Using KCL in above figure, we get,
)
In general form, we can write,

## Slide 11: Contd…
ECpE Department
Similarly, we can develop the current injections at buses 2,3, and 4 as:

## Slide 12: Contd…
ECpE Department
In matrix form, the equations of , , and can be written as,
Note:
, is an admittance matrix.
)

## Slide 13: Contd…
ECpE Department
Observations:
The Y matrix is symmetric, i.e.,
The off-diagonal elements are the negative of the admittance connecting bus bus , i.e.
The diagonal elements are the sum of the admittances connecting to bus plus the self-admittance of bus .

## Slide 14: Example: Find Admittance Matrix.
ECpE Department
The admittance matrix is:

## Slide 15: Power Flow Equations
ECpE Department
bus
Using KCL, the net injection at bus is,

## Slide 16: Power Flow Equations
ECpE Department
Net Power Injection

## Slide 17: Power Flow Equations
ECpE Department
Notes:
  ∠

## Slide 18: Power Flow Equations
ECpE Department
bus
Here, and are net power injections at bus . These equations are known as power flow equations

## Slide 19: Power Flow Equations
ECpE Department
How to solve the Power Flow Equations??

## Slide 20: Power Flow Equations
ECpE Department
How to solve the Power Flow Equations??
The Power Flow equations are solved by using iterative methods. The most commonly used iterative methods are:
Gauss Seidel Method
Newton-Raphson Method

## Slide 21: Power Flow Equations
ECpE Department
bus
Here, and are net power injections at bus .
  &

## Slide 22: Gauss Iteration
ECpE Department
In Gauss method, we need to rewrite our equation as: .
To iterate, we first make an initial guess of and solve.
until we find a fixed point. .
where,

## Slide 23: Example
ECpE Department
Solve . Use Gauss method.
Solution:
Rearranging the equation,
Initial Guess:

## Slide 24: Power Flow : Gauss Iteration Method
ECpE Department

## Slide 25: Example
ECpE Department
Solution:
Bus 1 is a swing bus

## Slide 26: Contd…
ECpE Department
We have,

## Slide 27: Contd…
ECpE Department

## Slide 28: Contd…
ECpE Department
Now,

## Slide 29: Gauss Method with Multiple Bus
ECpE Department
Considering, slack/swing Bus.
Note, these are Gauss Iterations

## Slide 30: Contd…
ECpE Department
Gauss - Seidel Iteration: Immediately use the new voltage estimates
But after we’ve determined we have a better estimate of its voltage, so it makes sense to use this new value. This approach is known as the Gauss-Seidel iteration.

## Slide 31: Advantages/ Disadvantages of Gauss Method
ECpE Department
Advantages
Each iteration is relatively fast
Computational burden is relatively low
easy to program.
Disadvantages
Has the tendency to miss solutions, especially for large systems
Need to compute using complex numbers.

## Slide 32: Newton – Raphson Method
ECpE Department
General form: Find an " " such that
For each guess of , define,
Represent by a Taylor series.
Linearization:

## Slide 33: Example
ECpE Department
Use to solve .
Solution,

## Slide 34: Contd…
ECpE Department
Use to solve .
Initial guess:
Therefore,

## Slide 35: Multi – Variable N-R method
ECpE Department
Define the solution .
Define
Expand using Taylor series
.
.
.

## Slide 36: Contd…
ECpE Department
n x n matrix of partial derivatives Also called as Jacobian Matrix (J(x))
In Matrix Form:

## Slide 37: Contd…
ECpE Department
So,

## Slide 38: Example:
ECpE Department
Solve for such that
where
Solution,

## Slide 39: Contd…
ECpE Department
Now, Initial Guess,

## Slide 40: Load Flow Analysis: N-R Method
ECpE Department

## Slide 41: Contd…
ECpE Department
Set ; make initial guess of (flat start: ).
1
End while
Note:
Jacobian elements are calculated by differentiating each function with respect to each variable.
For example: if is the bus real power equation,

## Slide 42: Contd…
ECpE Department
, when
When .

## Slide 43: Contd…
ECpE Department
When

## Slide 44: Thank You!
ECpE Department