## Slide 1: EE 303 – Electric Machines
Dr. Zhaoyu Wang (wzy@iastate.edu)
Dr. Salish Maharjan (salish@iastate.edu)
Department of Electrical and Computer Engineering
Iowa State University

## Slide 2: Three Phase Induction Motor
Dr. Zhaoyu Wang (wzy@iastate.edu)
Dr. Salish Maharjan (salish@iastate.edu)
Department of Electrical and Computer Engineering
Iowa State University

## Slide 3: Contents
Three phase induction motor types
Construction and principle of operation
Rotating magnetic field
Equivalent circuit of three phase induction motor
Torque speed characteristics
ECpE Department

## Slide 4: Three phase induction motor
ECpE Department
Invented by Nikola Tesla in 1888
Induction motor is the commonly used machine for converting electrical to mechanical energy.
Widely used in industry (e.g., water pumps, chillers, blowers, etc.) and home appliances (e.g., HVAC, Refrigerator, etc.)
Available size vary from half a kilowatt to thousands of kilowatts.
Advantages:
  Rugged construction
  Reliable operation
  Simple mechanism for torque and speed control

## Slide 5: Types and construction
ECpE Department
Squirrel cage induction motor
Slip ring induction motor
Main difference is the rotor construction

## Slide 6: Squirrel cage induction motor
ECpE Department
Stator
Constructed with laminated steel core
Holds the stator windings
Laminated steel core

## Slide 7: Squirrel cage induction motor
ECpE Department
Rotor
Constructed with laminated steel core
Contains no windings but conductor bars that are short circuited by an end ring.

## Slide 8: Slip ring induction motor
ECpE Department
Stator: Same as squirrel cage induction motor
Rotor
Constructed with laminated steel core
Holds the rotor windings.
The terminals of rotor windings are connected to slip rings.
The terminals of slip rings are brough out through stationary carbon brushes.

## Slide 9: Comparison of Squirrel cage and slip ring motor
ECpE Department
 | Features | Squirrel cage motor | Slip ring motor
1 | Rotor construction | Metallic bar are used in rotor No slip ring and brush rather the terminals of metallic bars are shorted by end rings. | Rotor windings are made of copper Slip ring and brush mechanism outlets the rotor windings’ terminals.
2 | Starting torque | Low | High
3 | Starting Current | High | Low
4 | Speed variation | Not easy, but could be varied by changing supply frequency | Easy to vary speed Speed can be changed by changing rotor resistance or supply frequency
5 | Maintenance | Almost ZERO maintenance | Requires frequent maintenance

## Slide 10: Principle of Operation
ECpE Department
Sequence of events
A voltage E = Blv is induced in each conductor while it is being cut by the flux (Faraday law).
The induced voltage immediately produces a current I, which flows down the conductor
Because the current carrying conductor lies in the magnetic field of the permanent magnet, it experiences a mechanical force (Lorentz force)
The force always acts in a direction to drag the conductor along with the magnetic field.
Thought Experiment

## Slide 11: Principle of Operation
ECpE Department
Sequence of events
If the conducting ladder is free to move, it will accelerate toward the right.
As it picks up speed, the conductors will be cut less rapidly by the moving magnet, with the result that the induced voltage E and the current I will diminish
Consequently, the force acting on the conductors wilt also decreases.
If the ladder were to move at the same speed as the magnetic field, the induced voltage E, the current I, and the force dragging the ladder along would all become zero.
Thought Experiment

## Slide 12: Rotating Magnetic Field
The three-phase winding produces magnetic flux along their axes.
ECpE Department
Stator windings
The resultant flux is given by vector sum of , , and .

## Slide 13: Rotating Magnetic Field
ECpE Department
At instant the three fluxes are given by;
Resultant flux,

## Slide 14: Rotating Magnetic Field
ECpE Department
At instant the three fluxes are given by;
resultant flux

## Slide 15: Rotating Magnetic Field
ECpE Department
At instant , the three fluxes are given by;
Phasor sum of and
Phasor sum of and gives the resultant flux

## Slide 16: Rotating Magnetic Field
ECpE Department
At instant , the three fluxes are given by;
Phasor sum of and
resultant flux
Phasor sum of and

## Slide 17: Resulting magnetic field
ECpE Department
The 3-phase supply in the stator winding produces a rotating field of constant value (= 1.5 , where is the maximum flux due to any phase).
The field is rotating in clockwise direction.

## Slide 18: Speed of rotating magnetic field
ECpE Department
The speed at which the rotating magnetic field revolves is called the synchronous speed (Ns), which is given by
Note refers to number of poles and f refers to frequency

## Slide 19: Slip
In practice, the rotor can never reach the speed of stator flux
If the relative speed between the stator field and rotor conductors is 0, then the rotor current are not induced and, hence, no torque to drive the rotor
The difference between the synchronous speed Ns of the rotating stator field and the actual rotor speed N is called slip and is given by
The slip is typically less than 15% in induction motors.
The induced rotor current frequency is , where is frequency of stator current.
ECpE Department

## Slide 20: Equivalent circuit of Three phase induction motor
ECpE Department
An induction motor may be considered a transformer with a rotating secondary (short-circuited).
The stator winding corresponds to a transformer primary and the rotor winding as secondary.

## Slide 21: Equivalent circuit of Three phase induction motor
ECpE Department
Hence the equivalent circuit can be written as:
Alternatively, can be written as:

## Slide 22: Equivalent circuit of Three phase induction motor
ECpE Department
K is the transformation ratio at standstill position of the rotor

## Slide 23: Torque equation
ECpE Department
Rotor Power
Rotor Power = T ω = 2πTN
T =

## Slide 24: Torque speed characteristics
ECpE Department

## Slide 25: Torque speed characteristics on varying R2
ECpE Department

## Slide 26
ECpE Department
Q&A
THANKS

## Slide 27: Synchronous Generator
Dr. Zhaoyu Wang (wzy@iastate.edu)
Dr. Salish Maharjan (salish@iastate.edu)
Department of Electrical and Computer Engineering
Iowa State University

## Slide 28: Synchronous Generator
ECpE Department
Synchronous generators convert the mechanical power of the turbine into electrical power
The source mechanical power could be a diesel engine, steam turbine, hydro turbines, etc.
Widely used in large scale power production in the range of several Mega Watts to Giga Watts.
Stator and Rotor of Synchronous generator of Grand Coulee hydroelectric power plant on the Columbia River in Washington State.

## Slide 29: Basic Topology
ECpE Department
Stator: support the placement of three phase winding as in Induction motor.
Stator winding are also referred to as armature winding.
Rotor: Unlike induction generator, the magnetic field is generated either by a permanent magnet or by applying dc current to rotor windings.
Rotor winding are referred to as field windings.
Stator
Rotor

## Slide 30: Types
ECpE Department
Salient-pole rotor
  Has protruding poles
  Air gap between stator and rotor is not uniform
  Designed for low-speed generator, e.g., Hydro
Cylindrical rotor
  Uniform airgap
  Designed for high-speed generator, e.g., steam generators

## Slide 31: Exciter system
ECpE Department
DC generator-based excitation system
Brushless excitation system/AC generator-based excitation system
Stator
Rotor
Exciter

## Slide 32: DC generator-based excitation system
ECpE Department
Supply DC power to field winding from a special DC generator mounted directly on the shaft of the synchronous generator.
DC generators have carbon brush, which require higher maintenance.

## Slide 33: AC generator-based excitation system
ECpE Department
Commonly referred as brushless excitation system
A small AC generator whose field circuits are mounted on the stator and armature circuits are mounted on the rotor shaft.
AC exciter output is rectified to DC by a 3-phase rectifier (mounted on the shaft) and fed into the main DC field circuit.
It is possible to adjust the field current on the main machine by controlling the small DC field current of the exciter generator (located on the stator).

## Slide 34: AC generator-based excitation system
ECpE Department

## Slide 35: Rotation speed of synchronous generator
ECpE Department
Where,
electrical frequency, in mechanical speed of magnetic field, in rpm = rotor speed, in rpm number of poles
For two pole generator to produce AC power at 60 Hz, it should be rotated at 3600 rpm

## Slide 36: Generation Voltage
ECpE Department
A uniform rotating magnetic flux () produced by rotating rotor at angular speed is
If is the number of coil in each stator windings, the emf induced in each phase would be
Peak voltage:
RMS voltage:

## Slide 37
ECpE Department
Q&A
THANKS